## Slide 1: EE4212 Brick-breaker project
Real-Time Embedded Systems
Academic Year 2016-2017
Paul-Edouard Sarlin
A0153124U

## Slide 2: Overview
Microblaze 0
Display
Microblaze 1
Model
Interrupt
GPIOs
Mailbox: model state
TFT
Debouncer & bar
Soft timer
Model loop with Ball
Col 1
…
Col 10
Display loop
Graphic primitives
Independent objects
Function call
Data via mutex
SW Signals
Hardware

## Slide 3
Model loop
Wake-up each brick column (chained semaphore)
Game
Running ?
Wait for trigger of collision check
Check collision with bar or boundaries
Try to acquire or release the golden resource
Check collision with the non-broken bricks
Signal if collision, and when it happened
Break the brick if validated, update score, trigger switch of golden columns
Wait for results of columns
Validate the soonest collision
(if any)
Change ball state if necessary
Update position of bar, check if collision
Prepare message to be sent to display
Wait a variable amount of time to keep the ball speed constant
YES
NO
Section switch
Signal via semaphore
BALL THREAD
COLUMN THREAD i

## Slide 4
In ball_thread:
  Pick the lowest iteration = soonest collision
  Send back the arbitration to the columns
  Update ball state
Collision checking for each column
If ball is not very far
  For each position between current and next frame:
  If ball is outside the zone of the column:
        Move to next position
  For each non-broken brick of the column:
        If ball is touching any edge or on any corner:
    Compute normal of the corresponding surface
    Send normal and corresponding iteration to ball
Signal to the ball that there is no collision
Similar procedure for collision with bar/boundaries

## Slide 5
Buttons debouncing, bar movement
If ISR enabled, wake-up buttons manager, disable ISR
If not woken-up by timer, sleep for DELAY, disable ISR
Get states of buttons
Wait for signal
If press is lower than DELAY_THRESHit is a jump!
Buttons are released ?
Timer elapsed ?
Start timer
Increase bar position
Wait for start
Signal when elapsed
Interrupt
Set constant bar speed
YES
NO
YES
NO
Enable ISR again
SW Timer
Buttons manager

## Slide 6
High FPS: up to 33
Coloured bar regions
Pseudo-random golden pattern
Random initial ball angle
Random initial golden columns
Ability to pause the game anytime
Double frame-buffer -> no flicker
Minimum coupling between uB0 and uB1 -> Can reset any of them at anytime
Salient features
Possible improvements
Draw all of the objects concurrently (threads) -> can increase FPS
Reset the game with a button (without resetting uB1)